## Slide 1: DRONE or NOT
BALASUBRAMANIAN G
24205037

## Slide 2
Project Overview — Drone vs Bird Classification using mmWave Radar
OBJECTIVE
Classify aerial targets (drone vs bird) in real-time using a 60 GHz FMCW mmWave radar, micro-Doppler spectrograms, and deep learning — without optical sensors or GPS.
HARDWARE
• TI IWR6843AOP EVM (Rev D+) — 60 GHz, 4 RX, 3 TX
• DCA1000EVM — Raw ADC data capture via LVDS + Ethernet
• mmWave Studio 2.1.1.0 + TI mmWave SDK 3.06.02
• Range resolution: 0.195 m | Max range: 50 m | 128 Doppler bins
3-PHASE APPROACH
Phase 1
Phase 1
ML Baseline
Random Forest on 77 GHz SAAB dataset 17 hand-crafted features → Acc 92.9%, AUC 0.974
Phase 2
Phase 2
Deep Learning
MicroDopplerCNN (SE-ResNet) on IEEE 60 GHz dataset STFT spectrograms → Mean Acc 87.3%, AUC 0.885
Phase 3
Phase 3
Live Capture
Raw ADC capture with IWR6843AOP + DCA1000 CFAR detection → CNN → Real-time prediction
Mistral Solutions | mmWave Radar Internship | Balasubramanian C | 2026

## Slide 3
Phase 1 — ML Baseline: Random Forest Classifier
DATASET — SAAB SIRS 77 GHz FMCW
• 130 samples: D1–D6 drones, 5 bird species, human walk/run
• IQ matrix (range-compressed) — 9.99 Hz chirp rate
• 99 binary samples used: 44 drone, 55 bird
• Stratified 5-Fold Cross-Validation
17 HANDCRAFTED FEATURES
Amplitude: mean, std, max, kurtosis, skewness, energy
Phase: std, mean_abs, max, kurtosis
Spectral: centroid, spread, entropy, peak_freq
Power: gate_power, power_variance, power_trend
RESULTS (5-Fold CV)
92.9%
Accuracy
0.919
F1 Score
0.974
ROC-AUC
TOP FEATURE IMPORTANCE
amp_mean
21.4%
gate_power
17.6%
amp_energy
16.9%
amp_std
12.1%
BEST MODEL PARAMS (GridSearchCV)
n_estimators=100 | max_features=sqrt
max_depth=None | min_samples_split=2
Classification: Drone vs Bird (Binary)
Mistral Solutions | mmWave Radar Internship | Balasubramanian C | 2026

## Slide 4
Phase 2 — Deep Learning: MicroDopplerCNN (SE-ResNet)
DATASET — IEEE 60 GHz FMCW (15.21 GB)
• 101 samples: 63 drone (DJI Mavic/P3P), 38 bird
• Range-Doppler maps: N_frames × 1000 × 128 complex
• Custom preprocessing → STFT spectrogram 64×64
MODEL ARCHITECTURE
Stem
Conv2d(1→32, 7×7) + BN + ReLU + MaxPool → 32×32
Stage 1
ResBlock(32) + Conv(stride=2) → 16×16
Stage 2
ResBlock(64)×2 + Conv(stride=2) → 8×8
Stage 3
ResBlock(128) + Conv(stride=2) → 4×4 [+ SE Attention]
Head
AvgPool + Dropout(0.3) + Linear(256→64) + Linear(64→2)
RESULTS — 3-FOLD STRATIFIED CV
Fold 1
Acc 85.0%
F1 0.880
AUC 0.760
Fold 2
Acc 91.0% ★
F1 0.930
AUC 0.974
Fold 3
Acc 86.0%
F1 0.900
AUC 0.920
Mean: Acc 87.3% F1 0.903 AUC 0.885
TRAINING SETUP
• AdamW (lr=3e-4) + CosineAnnealing | Batch=8, Epochs=80
• WeightedRandomSampler (3× oversample) + Class weights
• Augmentation: H-flip, Gaussian noise, brightness shift
• SE attention blocks, Global Average Pooling, Dropout
• Saved: best_model_fold2.pth
Mistral Solutions | mmWave Radar Internship | Balasubramanian C | 2026

## Slide 5
Phase 3 — Live Capture Pipeline & Real-World Results
END-TO-END PROCESSING PIPELINE
.bin Raw ADC
Parse IQ Data
Range FFT
Doppler FFT
CFAR Detect
STFT Spectro
CNN Predict
VALIDATION — LIVE CAPTURES (IWR6843AOP + DCA1000)
File
Scenario
SNR
CNN Result
Correct?
adc_data.bin
Hovering drone, 8.2 m
27.5 dB
Drone 99.6%
✓
adc_data_original_drone.bin
Flying drone (props spinning)
17.7 dB
Drone 98.8%
✓
adc_data_drone_static.bin
Drone placed, no rotation
15.0 dB
Drone 98.4%
⚠ (domain gap)
adc_data_plain.bin
Empty room
12.1 dB
No Target
✓
adc_data_bala1/2.bin
Hand wave
23.3 dB
Drone (wrong)
✗ → Fine-tune needed
NEXT: Fine-tune MicroDopplerCNN on own captures (Drone vs Not-Drone) using transfer learning to eliminate domain gap — 6 samples, LOO-CV.
Mistral Solutions | mmWave Radar Internship | Balasubramanian C | 2026